## Slide 1: Chapter 28 ICMPv6

## Slide 2: 28.1 Introduction
This new version, Internet Control Message Protocol version 6 ( ICMPv6 ), follows the same strategy and purposes of version 4
ICMPv6, however, is more complicated than ICMPv4
  Some protocols that were independent in version 4 are now part of ICMPv6
  Some new messages have been added to make it more useful

## Slide 3: Introduction (cont’)
Comparison of network layers in version 4 and version 6
Taxonomy of ICMPv6 messages

## Slide 4: 28.2 Error Messages
One of the main responsibilities of ICMP is to report errors
Four types of errors are handled
  Destination unreachable
  Packet too big
  Time exceeded
  Parameter problems

## Slide 5: Error Messages (cont’)
Destination unreachable message
  Code 0 : No path to destination
  Code 1 : Communication is prohibited
  Code 2 : Beyond the scope of source address
  Code 3 : Destination address is unreachable
  Code 4 : Port unreachable
  Code 5 : Source address failed (filtering policy)
  Code 6 : Reject route to destination

## Slide 6: Error Messages (cont’)
Packet-too-big message
  If a router receives a datagram that is larger than the maximum transmission unit (MTU) size of the network through which the datagram should pass.
    Discarding the datagram
    Then, sending an ICMP error packet to the source
  MTU field : informing the sender of the maximum size packet accepted by the network

## Slide 7: Error Messages (cont’)
Time-exceeded message

## Slide 8: Error Messages (cont’)
Parameter-problem message
  Offset pointer : 4 bytes
  Code fields
    Code 0 : Erroneous header field
    Code 1 : Unrecognized next header type
    Code 2 : Unrecognized IPv6 option

## Slide 9: 28.3 Informational Messages
Two of the ICMPv6 messages can be categorized as informational messages
  Echo request and echo reply messages
A host or router can send an echo request message to another host; the receiving computer or router can reply using the echo response message

## Slide 10: Informational Messages (cont’)
Echo-request message
Echo-reply message

## Slide 11: 28.4 Neighbor-Discovery Message
Several messages in the ICMPv4 have been redefined in ICMPv6 to handle the issue of neighbor discovery
The most important issue is the definition of two new protocols that clearly define the functionality of these group messages
  Neighbor-Discovery (ND) protocol
  Inverse-Neighbor-Discovery (IND) protocol

## Slide 12: Neighbor-Discovery Message (cont’)
Router Solicitation and Advertisement
  An option is added to allow the host to announce its physical address to make it easier for the router to respond.
Router-solicitation message
Router-advertisement message

## Slide 13: Neighbor-Discovery Message (cont’)
Neighbor-solicitation message

## Slide 14: Neighbor-Discovery Message (cont’)
Neighbor advertisement message

## Slide 15: Neighbor-Discovery Message (cont’)
Redirection message
  An option is added to let the host know the physical address of the target router

## Slide 16: Neighbor-Discovery Message (cont’)
Inverse-neighbor-solicitation message
Inverse-neighbor-advertisement message

## Slide 17: 28.5 Group Membership Message
The management of multicast delivery handling in IPv4 is given to the IGMPv3 protocol
In IPv6, this responsibility is given to the Multicast Listener Delivery protocol
  MLDv1 is the counterpart to IGMPv2; MLDv2 is the counterpart to IGMPv3
  The idea is the same as in IGMPv3, but the sizes and formats of the messages have been changed to fit the larger multicast address size in IPv6.

## Slide 18: Group Membership Message (cont’)
Membership query message format

## Slide 19: Group Membership Message (cont’)
Membership-report message format

## Slide 20: Summary
ICMPv6, like ICMPv4, is message-oriented; it uses messages to report errors, to get information, probe a neighbor, or manage multicast communication. However, a few other protocol are added to ICMPv6 to define the functionality and interpretation of the message.
We have divided all messages in the ICMPv6 into four categories: error messages, informational messages, neighbor-discovery messages, and group-membership messages.
Four types of error messages have been discussed: destination-unreachable, packet-too-big, time-exceed, and parameter-problem.

## Slide 21: Summary
Two type of informational messages have been discussed : echo-request and echo-response.
We discussed seven neighbor-discovery messages. The first five, router-solicitation, router-advertisement, neighbor-solicitation, neighbor-advertisement, and redirect are under the control of the ND protocol. The last two message, inverse-neighbor-solicitation and inverse-neighbor-advertisement are under the control of the IND protocol.
We discussed two group management messages : membership-query and membership-report. They are under the control of MDLv2 protocol