## Slide 1: Introduction to Software Defined Network (SDN)
April 9, 2013
CS Hong

## Slide 2: The Internet: A Remarkable Story
Tremendous success
  From research experiment to global infrastructure
Brilliance of under-specifying
  Network: best-effort packet delivery
  Hosts: arbitrary applications
Enables innovation in applications
  Web, P2P, VoIP, social networks, virtual worlds
But, change is easy only at the edge… 

## Slide 3: Inside the ‘Net: A Different Story…
Closed equipment
  Software bundled with hardware
  Vendor-specific interfaces
Over specified
  Slow protocol standardization
Few people can innovate
  Equipment vendors write the code
  Long delays to introduce new features
Impacts performance, security, reliability, cost…

## Slide 4: Networks are Hard to Manage
Operating a network is expensive (OPEX)
  More than half the cost of a network
  Yet, operator error causes most outages
Buggy software in the equipment
  Routers with 20+ million lines of code
  Cascading failures, vulnerabilities, etc.
The network is “in the way”
  Especially a problem in data centers
  … and home networks

## Slide 5: Rethinking the Networking

## Slide 6: Traditional Computer Networks
Data plane:
Packet streaming
  Forward, filter, buffer, mark,
  rate-limit, and measure packets
Notes: Maybe this is a better picture… though need some details of what happens in each plane… like in next slides… or, have both?

## Slide 7: Traditional Computer Networks
  Track topology changes, compute routes, install forwarding rules
Control plane:
Distributed algorithms
Notes: Maybe this is a better picture… though need some details of what happens in each plane… like in next slides… or, have both?

## Slide 8: Traditional Computer Networks
  Collect measurements and configure the equipment
Management plane:
Human time scale
Notes: Maybe this is a better picture… though need some details of what happens in each plane… like in next slides… or, have both?

## Slide 9: Death to the Control Plane!
Simpler management
  No need to “invert” control-plane operations
Faster pace of innovation
  Less dependence on vendors and standards
Easier interoperability
  Compatibility only in “wire” protocols!!
Simpler, cheaper equipment
  Minimal software

## Slide 10: Open Networking Foundation on SDN
… In the SDN architecture, the control and data planes are decoupled, network intelligence and state are logically centralized and the underlying network infrastructure is abstracted from the applications …

## Slide 11: Software Defined Networking (SDN)
API to the data plane
(e.g., OpenFlow)
Logically-centralized control
Switches
Smart,
slow
Dumb,
fast

## Slide 12: OpenFlow Networks

## Slide 13: Data-Plane: Simple Packet Handling
Simple packet-handling rules
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller

## Slide 14: Unifies Different Kinds of Boxes
Router
  Match: longest destination IP prefix
  Action: forward out a link
Switch
  Match: destination MAC address
  Action: forward or flood
Firewall
  Match: IP addresses and TCP/UDP port numbers
  Action: permit or deny
NAT
  Match: IP address and port
  Action: rewrite address and port

## Slide 15: Controller: Programmability
Network OS
Controller Application
Events from switches
Topology changes,
Traffic statistics,
Arriving packets
Commands to switches
(Un)install rules,
Query statistics,
Send packets

## Slide 16: Example OpenFlow Applications
Dynamic access control
Seamless mobility/migration
Server load balancing
Network virtualization
Using multiple wireless access points
Energy-efficient networking
Adaptive traffic monitoring
Denial-of-Service attack detection
See http://www.openflow.org/videos/

## Slide 17: E.g.: Dynamic Access Control
Inspect first packet of a connection
Consult the access control policy
Install rules to block or route traffic

## Slide 18: E.g.: Seamless Mobility/Migration
See host and send traffic at new location
Modify rules to reroute the traffic

## Slide 19: E.g.: Server Load Balancing
Pre-install load-balancing policy
Split traffic based on source IP
src=0*
src=1*

## Slide 20: E.g.: Network Virtualization
Partition the space of packet headers
Controller #1
Controller #2
Controller #3

## Slide 21: OpenFlow in the Wild
Open Networking Foundation
  Google, Facebook, Microsoft, Yahoo, Verizon, Deutsche Telekom, and many other companies
Commercial OpenFlow switches
  HP, NEC, Quanta, Dell, IBM, Juniper, …
Network operating systems
  NOX, Beacon, Floodlight, Nettle, ONIX, POX, Frenetic
Network deployments
  Eight campuses, and two research backbone networks
  Commercial deployments (e.g., Google backbone)

## Slide 22: A Helpful Analogy
From Nick McKeowns talk“Making SDN Work” at the Open Networking Summit, April 2012

## Slide 23: Mainframes
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface

## Slide 24: Routers/Switches
Vertically integrated
Closed, proprietary
Slow innovation
App
App
App
App
App
App
App
App
App
App
App
Horizontal
Open interfaces
Rapid innovation
Control
Plane
Control
Plane
Control
Plane
or
or
Open Interface
Specialized
Control
Plane
Specialized
Hardware
Specialized
Features
Merchant
Switching Chips
Open Interface

## Slide 25: Challenges

## Slide 26: Heterogeneous Switches
Number of packet-handling rules
Range of matches and actions
Multi-stage pipeline of packet processing
Offload some control-plane functionality (?)
access
control
MAC
look-up
IP
look-up

## Slide 27: Controller Delay and Overhead
Controller is much slower than the the switch
Processing packets leads to delay and overhead
Need to keep most packets in the “fast path”
packets

## Slide 28: Distributed Controller
Network OS
Controller Application
Network OS
Controller Application
For scalability and reliability
Partition and replicate state

## Slide 29: Testing and Debugging
OpenFlow makes programming possible
  Network-wide view at controller
  Direct control over data plane
Plenty of room for bugs
  Still a complex, distributed system
Need for testing techniques
  Controller applications
  Controller and switches
  Rules installed in the switches

## Slide 30: Programming Abstractions
Controller APIs are low-level
  Thin veneer on the underlying hardware
Need better languages
  Composition of modules
  Managing concurrency
  Querying network state
  Network-wide abstractions
Ongoing at Princeton
  http://www.frenetic-lang.org/
Controller
Switches

## Slide 31: Standardization Issues
ONF (Open Networking Foundation)
  Responsible for developing specifications of OpenFlow
  Even though SDO, it is also doing commercial oriented activities
  OF 1.3.1, OF-Config 1.1, OF-Test 1.0. OF-Hybrid 1.0 …
  With Google + Stanford related companies
IETF (Internet Engineering Task Force)
  I2RS WG
  Proposed SDN RG
  Cisco + IETF
ITU-T
  Carrier – SDN
  New Question (NV+SDN), Y.FNsdn
ETSI NFV ISG

## Slide 32: Standardization in ONF
Approval of OpenFlow Specification 1.3.1 approval (HP)
  Extensibility WG (Extensibility 1.3.1)
Approval of OF-CONFIG 1.1 (MS/NEC)
  Config & Mgmt WG
Testing & Interop 1.0 (Draft) (Ixia)
    Testing&Interop WG
Hybrid Programmable Forwarding Plane 1.0 (Huawei/Cisco)
  Hybrid WG (closed)
Arch WG (Big Switch)
  Top-Down Approach + (NB APIs)
Forwarding Abstraction WG (Brocade/Cisco)
  ASICs, NPUs, NP element Abstraction

## Slide 33: Standardization of IETF
SDN (Software-Driven Networking) BoF @IETF82
Technical Plenary@IETF84
  Technical Session: "Software Defined Networking"
Proposed SDN RG@IETF84, IETF85
IRS BoF@IETF85, now WG
More discussions @IETF86

## Slide 34: I2RS(IRS) @ IETF
Interface to the Routing System (i2rs)
Facilitating real-time or event driven interaction with the routing system through a collection of protocol-based control or management interfaces
Allowing information, policies, and operational parameters to be injected into and retrieved (as read or by notification) from the routing system
Users of the I2RS interfaces will be management applications, network controllers, and user applications that make specific demands on the network

## Slide 35: Standardization in ITU-T
Q.21 of SG13 (Future networks)
  Studying networks of 2015-20 ‘future networks’
  Has identified network virtualization as important components of 2015-20 telecom networks
  Hopes to be the pivot of SDN discussion in ITU-T
Draft Recommendations in Q.21
  Y.FNsdn, Framework of Telecom SDN Q4 2013)
  Y.FNsdn-fm, Requirements of formal specification and verification methods for software-defined networking (Q4 2013)
New Question for NV and SDN

## Slide 36: ETSI NFV ISG
1st Meeting
  15 to17January 2013 in Sophia Antipolis
Initial Discussions
  Architecture of the Virtualization Infrastructure (BT)
  Software Architecture for Network Functions (DT)
  Performance and Portability (Telefonica S.A.)
  Reliability & Availability (Verizon)
  Management & Orchestration (Telefonica S.A.)

## Slide 37: What is Network Function Virtualization

## Slide 38: Virtualization,Cloud and SDN
Rackspace offered Infrastructure-As-A –Service. Previously it was mostly Software-As-A-Service platform
VMWare
IPO 2007
IaaS Cloud
2008
Openflow
2008
SDN & Cloud Computing
2012~
Nicira Buy-out 2012
OpenStack
Management
2010
Integration of various virtualization and management SW started under the framework of OpenStack
Cloud Computing and SDN expands to Home Network, Data Center, LTE and etc.
Commercially
Meaningful CPU
Virtualization
Extended Mobility
(GTP, MME etc.)
Extended AAA
More Access Networks
Integration
Support for specific
applications
VMware buys Nicira and announced the network is the crucial for cloud computing.

## Slide 39: Tiers in SDN
Three-Tier Architecture of SDN
  Tier-1 : Forwarding entities and any software/hardware components comprising of them
  Tier-2 : Control and management entities for the Tier-1
    Control Layer
    Control functions Layer
  Tier-3 : Applications and services that take advantage of the infrastructures based on Tier-1 and Tier-2.

## Slide 40: SDN Use Cases
NTT Data: Intra Data Center
Google: Inter Data Center
Verizon: Optimized Routing
DT: Access (RAN, Fixed)

## Slide 41: HP Delivers SDN to Achieve Agility
Ability to Apply Business Logic to Network Behavior in Dynamic Fashion
Infrastructure Layer
SDN Architecture
Control
Layer
Application
Layer
Separate control and data plane; abstract control plane of many devices to one
Open standard-based programmatic access to infrastructure
Deliver open programmable interfaces to automate orchestration of network services

## Slide 42: HP Delivers SDN to Achieve Agility
Separate control and data plane; abstract control plane of many devices to one
Deliver open programmable interfaces to automate orchestration of network services
Open standard-based programmatic access to infrastructure
Deliver open programmable interfaces to automate orchestration of network services
Ability to Apply Business Logic to Network Behavior in Dynamic Fashion
Separate control and data plane; abstract control plane of many devices to one
Deliver open programmable interfaces to automate orchestration of network services
Open standard-based programmatic access to infrastructure
Network Device
Network Device
Network Device
Control & Data Plane Programmable
Interface (e.g., OpenFlow)
Network Applications
Network Applications
SDN Applications
Business Applications
Business Applications
Business Applications
(e.g., OpenStack, CloudStack)
Cloud Orchestration
SDN Controller
Programmable Open APIs
Infrastructure Layer
SDN Architecture
Control
Layer
Application
Layer

## Slide 43: References
Lecture Note by Jennifer Rexford http://www.cs.princeton.edu/courses/archive/spr12/cos461
Nick McKeown’s talk “Making SDN Work” at the Open Networking Summit, April 2012
MK Shin, HSN 2013 Presentation material of SDN
EK Paek, HSN 2013 Presentation material of SDN

## Slide 44: Open Source SDN Projects
Floodlight : an open source controller in Java
  Getting rapid acceptance in the OpenFlow community
Open vSwitch (OvS) : a multi-layer virtual switch released under the open source Apache 2.0 license
  Some of the originators of OpenFlow created OvS
OFTest : a framework and set of tests implemented in Python
  Giving people a way to validate the functionality of their OpenFlow switches by developed at Stanford
Indigo : Providing an implementation of OpenFlow on hardware switches by started at Stanford
FlowScale : an OpenFlow load-balancer
FlowVisor : a special purpose OpenFlow controller that acts as a transparent proxy between OpenFlow switches and multiple OpenFlow controllers
http://yuba.stanford.edu/~casado/of-sw.html

## Slide 45: Video on SDN
Mind the Gap
http://www.youtube.com/watch?v=Ho239zpKMwQ

## Slide 46: Thank you !