## Slide 1: OneM2M Challenges of M2M Security and Privacy

## Slide 2: Overview
M2M Abbreviation
oneM2M Architecture: a quick review
Security Architecture of M2M
Security Challenges
  Large variety of scenarios
  Any device in any deployment
  A device cannot make autonomous “judgement calls” on privacy
The solutions

## Slide 3
Abbreviation
  AE: Application Entity
  CoAP: Constrained Application Protocol
  CSE: Common Service Entity
  CSE-ID: Common Service Entity Identifier
  Mca: Reference Point for M2M Comm with AE
  Mcc: Reference Point for M2M Comm with CSE
  Mcc’: Reference Point for M2M Comm with CSE of different M2M Service Provider.
  Mcn: Reference Point for M2M Comm with NSE
  NSE: Network Service Entity
  TLS: Transport Layer Security
  DTLS: Datagram Transport Layer Security
  PSK: Pre-Shared Key
  PKI: Public Key Infrastructure

## Slide 4: M2M Architecture Model
General Concept
  M2M Layered model comprises three layer as shown in the picture:
Application Layer
Common Services Layer
Network Service Layer

## Slide 5: M2M Architecture Model
Functional Architecture

## Slide 6: M2M Architecture Model
The entity of each layer:
  Application Entity (AE), an entity in the application layer that implements an M2M application service logic.
  Common Services Entity (CSE), represent an instantiation of a set of “common service function” of the M2M environments.
  Network Services Entity (NSE), provides services from the underlying network to the CSEs.

## Slide 7: M2M Architecture Model
Reference Points
  Describe the links between entity.
  Mca, the links between an Application Entity (AE) and a Common Services Entity (CSE)
  Mcc, the links between two Common Services Entity (CSE)
  Mcn, the link between a Common Service Entity (CSE) and the Network Service Entity (NSE).
  Mcc’, the link between two Common Services Entities (CSE) from one M2M domain to different M2M domain.

## Slide 8: Security Architecture
Security Services
Security API (Mca, Mcc) (not specified in the present document)
Security Functions Layer
Identification and Authentication
Authorization
Identity Management
Security Association
Sensitive Data Handling
Security Administration
Secure Environment Abstraction Layer (not specified in the present document)
Security Environments Layer
Secure Environment n
Sensitive Data
Sensitive Function

## Slide 9: Security Architecture
Security Function Layer
  Contains a set of security function that are exposed at reference point (using security API)
  These security functions can be classified into six categories :
    Identification
    Authentication
    Authorization
    Security Association
    Sensitive Data Handling
    Security Administration

## Slide 10: Security Architecture
Security Environment Abstraction Layer
  Implements various security capabilities such as key derivation, data encryption/decryption, signature generation/verification, security credential read/write from/to the Security Environments
  The security function in this layer invoke the functions in order to do operations related to Secure Environments
  In addition, this layer also provides physical access to the Secure Environments

## Slide 11: Security Architecture
Secure Environment Layer
  Contains one or multiple secure environments that provide various security services related to sensitive data storage and sensitive function execution
  Example of sensitive data : SE capability, security keys, local credentials, identity information, and so on
  Example of sensitive function : data encryption, data decryption, and so on

## Slide 12: Design Principles of Security Architecture
Security Services are modular and configurable according to the needs of the hosting Common Service Entity
The architecture is split into several components and sub-components providing a modular design which enabled mapping of the architecture to different nodes and entities
The Secure Environment within the Common Service Entity is accessed via the Secure Environment Abstraction layer and shall hold all sensitive resources
The architecture may need to be adapted to be suitable for implementation in different entities
Security should consist of components relevant to fulfil the requirements of the respective node or entity and the intended use case

## Slide 13: Security Challenges
Large variety of scenarios
  “Assets” that need protecting can be unique to a deployment
    Content confidentiality, content integrity, anonymity, traffic efficiency
  Environment can be unique to a deployment
    Does wired or wireless transport layer provide adequate security?
    Tamper-resistance considerations
  Variety of authentication scenarios
    Pre-shared Key provisioned to both by end-points
    PKI/Certificate (asymmetric cryptography)
    Centralized authentication

## Slide 14: Security Challenges
Any device in any development
  Interoperability: agree on minimal set of cipher suites
  Credential management
    Provisioning at manufacture
    Human-assisted provisioning during deployment
    Remote provisioning of fielded devices
    Derivation from pre-existing credentials (e.g. transport network)

## Slide 15: Security Challenges
A device cannot make autonomous “judgement calls” on privacy
  M2M/IoT may expose information about our lives without our awareness
  Privacy = who can access information about me
  CSE needs to determine: “Should I allow access?”
  Can’t ask human to make case-by-case judgment call
  CSE needs clear rules

## Slide 16: Challenges & Solutions
Large variety of scenarios
Any device in any deployment
A device cannot make “judgment calls” on privacy
Secure communication
    various authentication options
Remote provisioning
    various authentication options
Access Control Policies
    expresses wide variety of rules

## Slide 17: Secure Communication: Example
CSE2
CSE1
AE2
AE1
Infrastructure
Domain
Field Domain
Sensor
Gateway
M2M SP’s Server
Web App
Server
E-Health Web-application

## Slide 18: Secure Communication: Example
CSE2
CSE1
AE2
AE1
Infrastructure
Domain
Field Domain
Sensor
Gateway
M2M SP’s Server
Web App
Server
AE1 passes sensor reading to CSE1
CoAP
UDP

## Slide 19: Secure Communication: Example
AE1 passes sensor reading to CSE1
CSE1 forwards sensor reading to CSE2
CSE2
CSE1
AE2
AE1
Infrastructure
Domain
Field Domain
Sensor
Gateway
M2M SP’s Server
Web App
Server
HTTP
TCP
CoAP
UDP

## Slide 20: Secure Communication: Example
AE1 passes sensor reading to CSE1
CSE1 forwards sensor reading to CSE2
AE2 retrieves sensor reading from CSE2
CSE2
CSE1
AE2
AE1
Infrastructure
Domain
Field Domain
Sensor
Gateway
M2M SP’s Server
Web App
Server
CoAP
UDP
HTTP
TCP
HTTP
TCP

## Slide 21: Secure Communication
Hop-by-Hop
  Transited CSEs see clear text
  Trusted to behave
CSE2
CSE1
AE2
AE1
Infrastructure
Domain
Field Domain
Sensor
Gateway
M2M SP’s Server
Web App
Server

## Slide 22: Secure Communication
CSE2
CSE1
AE2
AE1
Infrastructure
Domain
Field Domain
Sensor
Gateway
M2M SP’s Server
Web App
Server
CoAP
DTLS
UDP
Hop-by-Hop
TLS/DTLS v1.2
  DTLS if UDP transport

## Slide 23: Secure Communication
Hop-by-Hop
TLS/DTLS v1.2
  DTLS if UDP transport
  TLS if TCP transport
  Sometimes write (D)TLS or just TLS for both
CSE2
CSE1
AE2
AE1
Infrastructure
Domain
Field Domain
Sensor
Gateway
M2M SP’s Server
Web App
Server
HTTP
TLS
TCP
HTTP
TLS
TCP

## Slide 24: Secure Communication
Hop-by-Hop
TLS/DTLS v1.2
AE-CSE
  AE: TLS Client (C)
  CSE: TLS Server (S)
CSE2
CSE1
AE2
AE1
Infrastructure
Domain
Field Domain
Sensor
Gateway
M2M SP’s Server
Web App
Server
C
S
C
S

## Slide 25: Secure Communication
Hop-by-Hop
TLS/DTLS v1.2
AE-CSE
  AE: TLS Client (C)
  CSE: TLS Server (S)
CSE-CSE
  CSE1: TLS Client (C)
  CSE2: TLS Server (S)
CSE2
CSE1
AE2
AE1
Infrastructure
Domain
Field Domain
Sensor
Gateway
M2M SP’s Server
Web App
Server
C
S
C
C
S
S

## Slide 26: Authentication Options
Pre-Shared Key (PSK)
  TLS Client & Server provisioned with a shared key#
Certificate
  TLS Client & Server both have certificates
M2M Authentication Function (MAF)
  MAF operated by 3rd Party or M2M Service Provider
  TLS Client and MAF provisioned with a shared key#
  MAF assists authentication of TLS Client & Server
#This shared key can be remotely provisioned

## Slide 27: Certificates
Somewhat aligned with CoAP Security RFC7252
X.509/PKIX (RFC 5280)
RawPublicKey Certificates
  Contains only X.509 SubjectPublicKeyInfo element
  Suits less complex deployments & debugging
Certificates chaining to a trust anchor. E.g.
  Device Certificate (e.g. manufacturer issued)
  M2M SP issued certificate identifying CSE or AE

## Slide 28: Remote Provisioning
Process provisioning a shared key to two entities
M2M Enrolment Function (MEF)
  Assists remote provisioning
  Operated by 3rd Party or M2M Service Provider
Mechanisms for establishing shared key
  TLS Client & MEF perform (D)TLS, export shared key
    PSK
    Certificates
  Derived from Network Access credentials
    Network Access Provider assists in mutual authentication
    Generic Bootstrapping Architecture (GBA) 3GPP TS 33.220
Remote Provisioning goals are to generate Master Credential (Km) and corresponding Master Credential Identifier (KmId), shared by a CSE/AE and an M2M Authentication Function, to establish security associations between the CSE/AE and other CSEs and/or AEs

## Slide 29: Remote Provisioning
Defined by Remote Security Provisioning Framework. Remote Security Provisioning Framework consists of:
  Bootstrap Credential Configuration: phase of a Security Provisioning Framework in which the Bootstrap Credentials are pre-provisioned to the Enrolee and the M2M Enrolment function.
  Bootstrap Instruction Configuration: phase of a Security Provisioning Framework in which the Enrolee and M2M Enrolment Function are provided with identities (and any other relevant credentials) to enable the M2M Enrolment function to establish a Master Credential between the intended Enrolee and M2M Authentication Function.
  Bootstrap Enrolment Handshake: phase of a Security Provisioning Framework in which the Enrolee and M2M Enrolment Function perform mutual authentication.
  Enrolment Key Generation: phase of remote security provisioning Framework in which the Enrolee and M2M Enrolment function establish an Enrolment Key and Enrolment Key identifier.
  Integration to the Association Security Handshake

## Slide 30: Remote Provisioning Example
M2M Enrolment
Function
Enrolee
Enrolment Target
Enrollee: AE or CSE that requires remote provisioning of a symmetric key to be shared with an enrolment target.
Enrolment Target: CSE or AE with whom an Enrolee wishes to establish a symmetric key (master credential or pre-provisioned secure connection key) using remote security provisioning.

## Slide 31: Remote Provisioning Example
Mutual Authentication
M2M Enrolment
Function
Enrolee
Enrolment Target

## Slide 32: Remote Provisioning Example
Mutual Authentication Process

## Slide 33: Remote Provisioning Example
Mutual Authentication Process

## Slide 34: Remote Provisioning Example
Mutual Authentication
M2M Enrolment
Function
Enrolee
Enrolment Target
Generate Ke, KeId
Generate Ke, KeId
Ke, KeId
Ke, KeId
Ke: Enrolment Key
KeId: Enrolment Key Identifier

## Slide 35: Remote Provisioning Example
Enrolment Key Generation Process
MEF FQDN: M2M Enrolment Function Fully Qualified Domain Name.

## Slide 36: Remote Provisioning Example
M2M Enrolment
Function
Enrolee
Enrolment Target
Ke, KeId
Ke, KeId
KeId in (D)TLS Handshake

## Slide 37: Remote Provisioning Example
KeId (D)TLS Handshake process
Km: Master Credential
KmId: Master Credential Identifier
Kpsa: provisioned credential for M2M Security Association Establishment
KpsaId: provisioned credential for M2M Security Association Establishment Identifier

## Slide 38: Remote Provisioning Example
M2M Enrolment
Function
Enrolee
Enrolment Target
Ke, KeId
Ke, KeId
KeId in (D)TLS Handshake
KeId

## Slide 39: Remote Provisioning
M2M Enrolment
Function
Enrolee
Enrolment Target
Ke, KeId
Ke, KeId
KeId in (D)TLS Handshake
KeId
+ Enrolment
Target ID
+ Enrolment
Target ID
Shared Key
Shared Key

## Slide 40: Remote Provisioning Example
M2M Enrolment
Function
Enrolee
Enrolment Target
KeId in (D)TLS Handshake
KeId
Shared Key
Shared Key
Shared Key
Shared Key: a Pre-Shared Key that used to authenticate the enrollee
and Enrolment Target so the secure communication will establish.

## Slide 41: Remote Provisioning Example
M2M Enrolment
Function
Enrolee
Enrolment Target
Complete (D)TLS using Shared Key to verify provisioning
Shared Key
Shared Key

## Slide 42: Access Control Requirements
oneM2M uses a RESTful architecture
  API: request to perform an operation on a resource
  Operations: Create, Retrieve, Update, Delete
CSEs can’t make resource access judgement calls
CSE need clear rules dictating, for each resource
  WHO (which CSEs and AEs) are authorized to access,
  WHAT operations (see above), and under…
  WHICH circumstances (e.g. time, location of entity)

## Slide 43: Access Control Policies (ACP) Resources
Resource1
Resource4
Resource3
Resource2
ACP1
ACP3
ACP2
ACP Rule1
ACP Rule2
links
contains
ACP Rule3
Resource access is authorized upon satisfying at least one ACP rule in one of the linked ACPs

## Slide 44: Access Control Policies (ACP) Resources
Resource1
Resource4
Resource3
Resource2
ACP1
ACP3
ACP2
ACP Rule1
ACP Rule2
links
contains
WHO: entities
CSE-ID
AE-ID
WHICH: circumstances
    Time,
    location,
    IP address
WHAT: operations
Create,
Retrieve
Update
Delete
with conditions on
ACP Rule3
ACP rule is satisfied if WHO and WHAT and WHICH are satisfied by requesting entity, requested operation and circumstances